## Slide 1: CYCLIC REDUNDANCY CHECK (CRC)

## Slide 2: What is Cyclic Redundancy Check
Cyclic Redundancy Check method is a powerful error detection method
It can detect all odd errors, single and duble bit errors and burst errors of length
equal to polynomial degree
It is based on binary division

## Slide 3: Cyclic Redundancy Check
Error detection in pure data is likely impossible that’s why this method is used
In cyclic redundancy check error detection method we use a redundant variable
which is used to detect errors in message
Total bits sent to receiver – Message Bits + CRC Bits

## Slide 4: Clyclic Redundancy Check Example
Message bits - 1010101010
Divisor – x4+x3+1(polynomial)
Converting divisor or polynomial to binary
1*x4+1*x3+0*x2+0*x1+0*1 = 11001

## Slide 5: Dividing the message bit via divisor
Appending bits to the message
Appending bits equals to the maximum degree of polynomial divisor.
In case if the divisor is in binary form then the appending bits will be
Total bits in divisor - 1

## Slide 6: Dividing the message bits via divisor
Final Message bits – 10101010100000
Dividing the final message bits via divisor
10101010100000/11001
Division via ‘XOR’ Operation
XOR 1 0 = 1
0 1 = 1
1 1 = 0
0 0 = 0
Reminder = 000010

## Slide 7: Valid data code bits
Original message 10101010
Appending the reminder value in place of CRC bits
1010101010 0000
Final message bits =
Reminder = 000010
Sent message bits = 10101010100010

## Slide 8: Division
10101010100000
11001
11001
011000
11001
000011010
11001
00011000
11001
000010
Reminder

## Slide 9: Message received by the reciever
Sent Message Bits – 10101010100010
10101010100010
11001
Reminder will be zero then no error occurs
And if the reminder is not zero then any error occurs in the message sent by the sender
Reminder zero